## Slide 1: Dragonfly Topology and Routing

## Slide 2: Outline
Background
Motivation
Topology description
Routing
  Minimal Routing
  Valiant Routing
  UGAL/G Adaptive Routing
  Indirect Adaptive Routing
    Credit Round Trip
    Reservation
    Piggyback
    Progressive
  Performance Comparison

## Slide 3: Background
As memory and processor performance increases, interconnect networks are becoming critical
Topology of an interconnect network affects the performance and cost of the network
A good interconnect network, exploits emerging technologies

## Slide 4: Motivation
Increasing router pin bandwidth
  High-radix routers
Development of active optical cables
  Longer links with less cost per unit distance
Using above technology advancements, we can build networks with higher performance. How?

## Slide 5: Motivation
Reduced network diameter and latency

## Slide 6: Motivation
Problem 1: Number of ports in each router is limited (64, 128, …)
  We want much higher radices (8K – 1M nodes)
Problem 2: Long global links between groups are expensive and dominate network cost
  We should minimize number of global channels traversed by an average packet

## Slide 7: Motivation
Solution: use group of networks connected to a sub-network as a virtual high-radix router
  All minimal routes traverse at most only one global link
  Length of global links are increased to reduce the cost

## Slide 8: Dragonfly Topology
K = radix of each router = p + a + h - 1
K’ = virtual router radix = a(p + h)
N = ap(ah + 1)
  [Kim et al. ISCA08]

## Slide 9: Topology Description
Three-level architecture:
  Router, Group, System
Arbitrary networks can be used for inter-group and intra-group networks
K’ >> K
  Very high radix virtual routers
  Enables very low global diameter (=1)
To balance channel load on load balanced traffic:
  a = 2p = 2h

## Slide 10: Topology Variations
  [Kim et al. ISCA08]

## Slide 11: Minimal Routing
Step 1 : If Gs ≠ Gd and Rs does not have a connection to Gd, route within Gs from Rs to Ra, a router that has a global channel to Gd.
Step 2 : If Gs ≠ Gd, traverse the global channel from Ra to reach router Rb in Gd.
Step 3 : If Rb ≠ Rd, route within Gd from Rb to Rd.

## Slide 12: Minimal Routing

## Slide 13: Minimal Routing
Good for uniform traffic
  All links are used evenly
Link saturation happens on adversarial traffic
  Global ADV
  Local ADV
Load balancing mechanism needed to distribute traffic

## Slide 14: Valiant Randomized Routing
Step 1 : If Gs ≠ Gi and Rs does not have a connection to Gi, route within Gs from Rs to Ra, a router that has a global channel to Gi.
Step 2 : If Gs ≠ Gi traverse the global channel from Ra to reach router Rx in Gi.
Step 3 : If Gi ≠ Gd and Rx does not have a connection to Gd, route within Gi from Rx to Ry, a router that has a global channel to Gd.
Step 4 : If Gi ≠ Gd, traverse the global channel from Ry to router Rb in Gd.
Step 5 : If Rb ≠ Rd, route within Gd from Rb to Rd.

## Slide 15: Valiant Routing

## Slide 16: Valiant Routing
Balances use of global links
Increases path length by at least one global link
Performs poorly on benign traffic
Maximum throughput can be 50%

## Slide 17: UGAL-G/L Adaptive Routing
Choose between MIN and VAL on a packet by packet basis to load balance the network
Path with minimum delay is selected:
  Queue length
  Hop count
UGAL-L uses local queue info at the current router node
UGAL-G uses queue info for all global channels in Gs

## Slide 18: UGAL Adaptive Routing
Measuring path queue length is unrealistic (UGAL-G)
Use local queue length to approximate path queue length
Local queues only sense congestion on a global channel via backpressure over the local channel
  Requires stiff backpressure

## Slide 19: Adaptive Routing
  [Jiang et al. ISCA09]

## Slide 20: Indirect Adaptive Routing
Improve routing decision through remote congestion information
Four methods:
  Credit Round Trip
  Reservation
  Piggyback
  Progressive

## Slide 21: Credit Round Trip
  [Jiang et al. ISCA09]

## Slide 22: Credit Round Trip
Delay the return of local credits to the congested router
Creates the illusion of stiffer backpressure
Drawbacks:
  Remote Congestion is still sensed through local queue
  Info is not up to date
Source
Router
Congestion
Delayed
Credits
Credits
MIN
GC
VAL
GC
  [Jiang et al. ISCA09]

## Slide 23: Reservation
Reserve bandwidth on minimal global channel
If successful send the packet minimally
If not, route non-minimally
Drawbacks:
  Needs buffer at source router to hold waiting packets
  Packet latency increased by round-trip time of RES flit
  RES flits can create significant load on source group
Source
Router
Congestion
RES
Flit
RES
Failed
MIN
GC
VAL
GC
  [Jiang et al. ISCA09]

## Slide 24: Piggyback
Broadcast link state info of GCs to adjacent routers
Each router maintains the most recent link state information for every GCs in its group.
routing decision is made using both global state information and the local queue depth
congestion level of each GC is compressed into a single bit (SGC)
Drawbacks:
  Consumes extra bandwidth
  Congestion information not up to date due to broadcast delay
  [Jiang et al. ISCA09]
Source
Router
Congestion
GC
Busy
GC
Free
MIN
GC
VAL
GC

## Slide 25: Progressive
Re-evaluate the decision to route minimally at each hop in the source group
Non-minimal routing decisions are final
The packet is routed minimally until congestion encountered. Then it routes non-minimally
Drawbacks:
  Adds extra hops
  Needs an additional virtual channel to avoid deadlocks
Source
Router
Congestion
MIN
GC
VAL
GC
  [Jiang et al. ISCA09]

## Slide 26: Steady State Traffic: Uniform Random
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
100
120
140
160
180
200
220
240
260
280
300
Throughput (Flit Injection Rate)
Packet Latency (Simulation cycles)
Piggyback
Credit Round Trip
Progressive
Reservation
Minimal
  [Jiang et al. ISCA09]

## Slide 27: Steady State Traffic: Worst Case
0
0.1
0.2
0.3
0.4
0.5
100
150
200
250
300
350
400
450
Throughput (Flit Injection Rate)
Packet Latency (Simulation cycles)
Piggyback
Credit Round Trip
Progressive
Reservation
Valiant’s
  [Jiang et al. ISCA09]